## Slide 1: NTAG I²C Your entryway to NFC: The simplest, most cost-effective NFC solution
Feb, 2016

## Slide 2
NFC | what and why?
NFC - like a wireless (read/write) memory stick with a unique serial number for identification
500 million NFC-enabled smartphones shipped in 2014
By 2018, there will be 1.7 billion NFC-enabled smartphones in the market
(ABI Research, 2013)

## Slide 3: NFC | Principal of operation
Same fundamental principle as RFID, contactless smart cards or access control badges
Reader (e.g. mobile device) provides power, initiates RF communications & captures data from the tag (or programs data into the tag)
13.56MHz
Like a transformer
READER
TAG

## Slide 4: Conventional tag
NFC
EEPROM
Analog
Data

## Slide 5: NTAG I2C | Connected tag - EEPROM
NFC
EEPROM
Analog
Data
(1KB)
VOUT
Data
SRAM
I/F
Logic
Microcontroller
VCC
GND
FD
I2C
Harvested power
Interrupt
Serial data

## Slide 6: NTAG I2C | Connected tag – SRAM buffer
NFC
EEPROM
Analog
Data
(1KB)
VOUT
Data
SRAM
I/F
Logic
Microcontroller
VCC
GND
FD
I2C
Harvested power
Interrupt
Serial data

## Slide 7: NTAG I2C | Detailed architecture
For power management, the whole system may be powered up upon Field Detection
FD is asserted low when the field is detected; PMU receives interrupt, switches VCC on NTAG and µC; µC activates I²C
Alternatively, VOUT (harvested energy) may be used for low power devices as source of power.

## Slide 8: NTAG I2C | NFC for embedded applications
Notes: Key attributes:
Zero power operation – configure without applying power or read diagnostics when the unit is inoperable
Enhance the user experience by using the NFC enabled Smart Phone for the touchscreen and network connectivity, providing a right GUI with minimal impact to the product cost
Easy pairing an commissioning to wireless networks
When consumables are required, load the tag with trusted eRetailer URLS for authenticated replenishment

## Slide 9: NTAG I2C | Key attributes at a glance
Improved registration response
  Automate warranty card registrations (seconds vs. minutes, uptick in marketing value)
Remote user interface
  Extended a rich user interface on a NFC mobile phone without the cost of a touch display
Easy pairing & connectivity
  Provide cost effective wireless connectivity or complement BT / WiFi connectivity with easy pairing
New revenue options
  Open an avenue for authenticated consumable replenishments (new revenue stream for original or preferred partner branded consumables)
Wireless configuration & customization
  Enable wireless product configuration, including optional upgrades from a generic board
  Customize and personalize products to add a special touch
Enhanced maintenance
  Electronic serialization
  Improve maintenance (elaborate on error codes, provide diagnostics, enable service videos & manuals, etc.)
  Easily schedule service (automate service requests, provide vital info, born-on date, & provide diagnostics)
  Enable service technicians to wirelessly calibrate or download firmware without LAN or WiFi connectivity
  Access appliance info/diagnostic codes/service history, even without power

## Slide 10
NTAG I2C enables
HIGH-END FEATURES…
AT MASS MARKET PRICES

## Slide 11: NFC | complementary to other wireless options
NFC Benefits
Pair by intent:
NFC reader initiates communication versus broadly broadcasting
Low-power:
NFC transponder (tags) harvest energy from reader field, no batteries required
Cost:
Hi feature set, low BoM cost

## Slide 12
Auto power / pair
  Use Field Detect
  Tap to power
  Tap for user-friendly mobile device pairing
  Easily pair to intended item where multiples may exist
Convenient activation / pairing

## Slide 13: NTAG I2C Use Case – Wireless commisioning
Notes: Use the phone to transfer network credentials – tap on the wireless router to extract the SSID/PW and again on the extender or end node to transfer the credential
Helps alleviate open broadcast security issues associated with traditional WPS methods of pairing

## Slide 14: NTAG I2C Use Case – Wireless Pairing
WiFi Pairing
Bluetooth Pairing
Home automation commissioning
Notes: As noted on slides – for commissioning and pairing

## Slide 15: Learn more – tap icon below

## Slide 16: NTAG I2C | Washing machine animation
Notes: Animation of various use cases for an appliance

## Slide 17
Enhanced feature set
  Add richly enhanced product features using mobile device as extended GUI
  Define and assign “favorite” user settings
Extended product features
Notes: As noted on slide

## Slide 18
User-defined access
  Set for administrative or general user access
  Enhance security by limiting unauthorized settings
  Remotely grant temporary access provisions
Administrative access
Notes: As noted on slide

## Slide 19
Easy registration
  Tap to extract model/serial number
  Auto-fill personal info
  Electronically submit to cloud
  Link opportunity for consumable replenishment
Easy registration & convenient replenishment
Notes: Tap device for the serial and model number
Auto-fill with your personal info, stored in your phone, submit to register within seconds
Tap again to transfer your registration info and date into the device for warranty purposes
Link customer to cloud based eRetailers for authentic replenishments

## Slide 20: NTAG I2C Demo | Washing Machine Use-Cases
Extended user interface / features
User-friendly service
Notes: Extended GUI elaborated
Instructional videos or manuals can be downloaded after reading the error code and model number, then looking up in the cloud

## Slide 21
Zero-power configuration
Bidirectional communication
Configuration / calibration
  Fewer production derivatives
  Higher supply flexibility
  Service diagnostics & contactless calibration
Notes: Typically can provide up to about 10mW of power, e.g. 2.7V at about 3.5mA or 2V at about 5mA)
Great for powering low power micro for diagnostics or for customization or configuration without external power

## Slide 22
Convenient maintenance & diagnostics
  User-friendly service references / tips / videos
  Extract error diagnostics & provide helpful interactive user service hints
Self-serve maintenance
Notes: As noted on slide

## Slide 23
Bridge- mode
  NTAG I2C serves as a modem, using SRAM buffer
  Unlimited data exchange & unlimited write cycles
  Eliminated connectors & ease machine access
Firmware update
Notes: As note on slide – no limitations on on files size with SRAM buffer and no limited write cycle concerns.

## Slide 24: NTAG I2C website | www.nxp-rfid.com/ntag-i2c
Notes: Plentiful design resources available for Use-Case and Application reference as well as for cut-and-paste designs

## Slide 25: Resources | General NTAG I2C
Notes: The general resource section include FAQ’s, the data sheet, antenna design guidelines, videos, a brochure and presentations for registered user’s to access

## Slide 26: Reference Designs | NTAG I2C Explorer Kit
Notes: The NTAG I2C Explorer Kit Reference Design include design files for the Explorer Board, the various antennas, etc.
Files include Schematics, Gerbers, BoM’s, firmware, Source Code, and an extensive user’s guide for a detailed overview of the reference design
Though the Reference Design is not readily available for purchase or sampling, the designs are available and help in importing to your application
The LED Demo is a scaled version (e.g. without a LCD display) and is readily available through the eSample desk – see your distribution representative for additional information

## Slide 27: Resources | NTAG I2C Brochure
20-page brochure outlining applications, use-cases, features and benefits

## Slide 28: NTAG I2C LED demo kit (OM5569/NT312D)
Contents:
LED demo board
Class 5 antenna board
(10) 1KB NTAG I2C samples
Available through eDemoboard page
Reference:
http://www.nxp.com/demoboard/OM5569.html
Notes: Here’s the available demo kit including a LPC 812 micro, a LM75 Temp Sensor, LED’s, momentary switches ,and the NTAG I2C.

## Slide 29: NTAG I2C | LED Demo – RF  I2C direction
RF  I2C data direction
Press a color on “Board Configuration” on the app
Confirm RGB LED on LED Demo illuminates
Notes: Simple instructions on how to use the LED demo – showing the RF to I2C direction

## Slide 30: NTAG I2C | LED Demo – I2C  RF direction
I2C  RF data direction
Press a numbered switch on the LED Demo Board
Confirm the appropriate numbered rectangle on the app illuminates
Notes: Simple instructions on how to use the LED demo – showing the I2C to RFdirection

## Slide 31: NTAG I2C | LED Demo Temperature
Temperature
The LM75A temp sensor provides temperature in °C to the app via SRAM
The app calculates the temp and displays it in °F
Notes: Simple instructions on how to use the LED demo – showing the SRAM feature by reading temp

## Slide 32: NXP Connected Tags | Product offerings
Product Type | NT3H1101W0FHK | NT3H1101W0FTT
Description | NTAG I2C 1KB | NTAG I2C 1KB
Delivery Form | SOT902 | TSSOP8
Sales 12NC | 9353 028 42125 | 935 305 481 118
MOQ | 4kpcs | 2.5kpcs
Notes: Here are the min order quantity and available orderable packages of the NTAG I2C

## Slide 33: Summary
NFC is becoming ubiquitous in today’s smart phones
  500 million NFC enabled phones shipped in 2014
  NTAG I2C connected tags enable
    Feature-rich, cost effective soloutions
    Passive, low power operation
    Private / tap-by-intent interaction for embedded sytems
  Use cases
    Improved registration response
    Zero-power interaction
    Extended user-interface
    Wireless configuration and customization
    Enhanced maintenance and servicability
  Resources to get started
    Visit www.nxp-rfid.com/ntag-i2c for additional information
Notes: Summary of the presentation

## Slide 34: NTAG I²C plus

## Slide 35: NTAG I²C vs. NTAG I²C plus
Feature | NTAG I²C | NTAG I²C plus | Comment – What is new
Backward compatibility |  |  | New features are backward compatible to NXPs NTAG 21xF family
Interoperability with NFC enabled devices | + | +++ | All features are accessible/useable via sector 0
Memory access protection via NFC interface | + | +++ | (Optional) 32-bit password to write or read & write protect (parts of) EEPROM and/or SRAM Disable NFC access at all Disable NFC access to sector 1
Memory access protection via I²C interface |  |  | Restrict access to protected area from I²C perspective to read-only or no access at all
ECC based Originality Signature |  |  | Genuine and simple authentication scheme
Pass-through performance | + | +++ | Four times higher pass-through performance due to introduced FAST WRITE command
Wave-soldering assembly |  |  | On top of XQFN8 and TSSOP8 package, we offer SO8 package
Temperature range | -40°C to 95°C | -40°C to 105°C | For industrial applications
Supply Voltage Range | 1.8V to 3.6V | 1.67V to 3.6V | For single cell supplied devices - like wearables

## Slide 36: NTAG I²C plus features
NFC Forum Type 2 Tag (will be possible to certify)
Dual interface
  NFC & I²C (100 & 400kHz) interface
  50 pF input capacitance
Either 888 or 1912 Byte EEPROM
Energy harvesting functionality to power external device
PIN to PIN outlines & fully backward compatible
What´s NEW?
Pass Through Mode performance increased by factor 4 in NFC to I²C with FAST_WRITE command to SRAM
Authentication: Originality signature based on ECDSA (compatible with the NTAG 21x(F) family)
Access protection: Optional 32-bit password on the full EEPROM and the SRAM buffer
SO8 package & XQFN8 package (1,6*1,6*0,5mm) & TSSOP8
Increased Compatibility with legacy NFC devices (SRAM and CONFIG on sector 0)

## Slide 37: NTAG I²C plus Memory Access Rights
888/1912 Byte User Memory
*: I²C Address on block 0 byte 0 only writeable, but not readable
RF
I²C
RF
I²C
Memory
Read
Write
Serial Number
-
I2C
Address *
Lock Bytes / CC
OTP, Lockable
User Memory
Lockable, PWD
AP
Lockable, PWD
AP
SRAM
Lockable
Configuration
PWD
Lockable, PWD
Session Register
-
RF Sector | Byte number within a page |  |  | 
Hex | 0 | 1 | 2 | 3
0h | Serial number (SNR) |  |  | 
 |  |  | Static lock bytes | 
 | Capability Container (CC) |  |  | 
 | User memory (888/1912 Bytes) |  |  | 
 | Dynamic lock bytes (3 Bytes) |  |  | 
 | Default Configuration (8 Bytes) |  |  | 
 | SRAM memory (64 Bytes) in Pass Through mode only |  |  | 
3h |  |  |  | 
 | Session registers (8 Bytes) |  |  | 
PWD
PWD
Notes: Password protection is excluded for Dynamic lock bits, session registers and mirrored SRAM pages.

## Slide 38: Special memory block: Configuration bytes
NC_REG = NTAG Control Register, controls enabled functions
  SILENT MODE
  PASS THROUGH MODE (now is documented and is useable)
LAST_NDEF_BLOCK: Address of end of NDEF message (FD pin trigger)
SRAM_MIRROR_BLOCK: Address of mirrored SRAM (for SRAM_MIRROR)
WDT_LS: Watchdog timer control for I²C communication (16 bit) LSB
WDT_MS: Watchdog timer control for I²C communication (16 bit) MSB
I2C_CLOCK_STR: I²C Clock Stretching
REG_LOCK: Prevent Write Access from RF / I²C
Back

## Slide 39: NTAG I²C plus RF commands
Proprietary (need App) | 
FAST_WRITE | Writes 64 bytes to SRAM (only pass-through mode)
READ_SIG | Returns IC specific 32-byte ECC signature (NXP)
PWD_AUTH | Access to protected area (AUTH0, NFC_PROT – defines protection, AUTHLIM–unsuccessful attempts)
The RF-interface is based on the ISO/IEC 14443 Type A standard for contactless smart cards. All memory functions are operated in the ACTIVE state.
NEW:

## Slide 40: Pass-through – speed test
Heavily dependant on the NFC readers used
Mobile phones typically slower than NFC readers. FAST_WRITE improved speed.
Chart: Speed test: NTAG I²C plus and Android NTAG I²C Demo App
| Sonxy Xperia Z1 | Nexus 5 | Nexus 4 | Galaxy Nexus | Samsung Galaxy S4 mini | Samsung Galaxy S4 | Samsung Galaxy Young 2 | Nexus S | Motorola Moto X V2 | Samsung Galaxy S3 | Nexus 7 | Samsung S5 NEO | Samsung Galaxy S6 | Huawei P7
WRITE | 0.22123 | 0.26786 | 0.27663 | 0.26596 | 0.34618 | 0.3249 | 0.37133 | 0.27663 | 0.34643 | 0.32524 | 0.21163 | 0.36361 | 0.37286 | 0.56036
FAST_WRITE | 0.86307 | 0.88038 | 0.89853 | 0.90483 | 1.7704 | 1.9077 | 1.9476 | 2.0405 | 2.1376 | 2.2293 | 2.2293 | 2.3106 | 2.4907 | 3.0952
FAST_READ | 0.86856 | 0.87216 | 0.92397 | 0.94721 | 1.8541 | 1.788 | 1.9245 | 2.2023 | 2.3368 | 2.301 | 2.301 | 2.0837 | 2.5716 | 3.2598

## Slide 41: Energy harvesting
With energy harvesting a microcontroller can be supplied with power
  Typically >5mA @2V
  Up to 13mA in case of strong NFC readers (not NFC phones)
Power up can be controlled by Field Detection for further power management optimization
  FD goes low when field is detected; PMU receives interrupt, switches on VCC on NTAG and µC; µC starts communication on I²C
Feb-16
NTAG I²C plus
VCC
LA
LB
FD
SDA
SCL
SRAM
NVM
open drain
PMU
(Power Management Unit) optional, can be in the µC
2
3
4
µController
1
VOUT

## Slide 42: Energy harvesting – achievable power

## Slide 43: Flexible Memory Access Management (1/2)
RF/NFC perspective
  32-bit password
  16-bit PACK (password auth. acknowledge response)
  Optionally limited number of unsuccessful authentications
    up to 27 negative attempts
  Write or read/write memory access can be restricted to be allowed only after password authentication
  Pass-through can be restricted to be allowed only after password authentication
  Memory can be split in open and protected segments
    Memory boundary is configurable
RF/NFC perspective
I²C perspective

## Slide 44: NTAG I²C plus Silent Mode
With the bit NFCS_I2C_RST_ON_OFF (NC_REG) below features are enabled the same time:
  I²C soft reset
- Helps if interface gets stuck due to heavy bus interference
- „STOP“ after each start symbol mandatory
  NFC silence feature
- NFC demodulator is turned off/disabled
- Tag „disappears“ even if present in the field

## Slide 45: NTAG I²C plus general application circuit
R1 + R2 = general I²C Bus Pullup, only ONE needed per I²C bus, sized according to bus load (usually 1k-10k)
R3, FD pin pullup, use any value above ~1k (e.g.: 20k)
C1 = 100nF – 200nF (recommended). For larger caps measures to reduce the start-up-current are needed (e.g. Serial resistor of 20 Ohm between the EH pin and the first cap)
C2 – optional, only needed if resonance of antenna alone is too high – target resonce should be around 13,5-14,5 Mhz – beware of influence of surrounding!
µController
NTAG I²C plus
VCC
LA
LB
FD
SDA
SCL
SRAM
NVM
EH
R1
R2
R3
C1
VCC
C2
PMU
VOUT

## Slide 46: NTAG I²C plus standby power saving
For RF communication the tag works completely passive – no external power needed
Power on VCC (typical 155µA) is needed only for:
  I²C communication
  Usage of SRAM
How to save power:
  Turn VCC off unless I²C communication or SRAM is needed
  MCU can detect RF activity using:
    Vout – goes high in case the tag is exposed to RF field
    FD pin – can be configured to go low (open drain – needs pullup) on RF activity
 Standby power can be reduced to zero! (in case of using Vout)

## Slide 47: NTAG I²C plus demokits variants OM5596/NT322(X)
Demokit name | Contents
OM5569/NT322E | NTAG I²C plus Explorer Kit with Field Detector Board, flex antenna and SO8 samples
OM5569/NT322ER | NTAG I²C plus Explorer Kit Field Detector Board, flex antenna, NFC reader and SO8 samples
OM5569/NT322F | NTAG I²C plus Flex Antenna Kit with 3 different flex antennas only and SO8 samples

## Slide 48: NTAG I²C plus Explorer Board OM5569/312E
Components:
  LPC11U24
  RGB-LED
  Buttons
  Temp-Sensor LM75B
  LCD
  micro-USB
Shows:
  Energy Harvesting
  LED Demo with interactive LED control and Buttons + Temp feedback
  Zero-Power Configuration (switch LED on depending on NDEF)
  SRAM and EEPROM speed measurement
  NDEF message read write with NDEF content display on LCD
  I²C memory read/write with a windows GUI (I²C-USB-Bridge)
  MCU firmware flashing via NFC
Antenna Design Files Class 4, 5, 6 + Flex
PCB Design Explorer Board + Firmware
Availability: NXP webpage

## Slide 49: NTAG I²C plus - general support tools
PC-Software
  RFIDDiscover Lite 4.1.5 supports NTAG I²C plus
  Peek & Poke
  PC App for Explorer board
  Android project for Eclipse (portable to Android Studio)
  NFC TagInfo by NXP (in Google PlayStore)
  NXP TagWriter by NXP (in Google PlayStore)
  Android: “NTAG I2C Demo” (will be available in Google PlayStore)
  Controlling LEDs and showing communication speed available on Google Play store „NTAG I2C Demo“
  Improved FAST_WRITE
  Reading temperature from temp. sensor
  Writing data to LCD
  Firmware upload
  Password authentication
(links active/online
mid February)

## Slide 50: NTAG I2C Explorer board firmware
The delivered NTAG I2C Explorer board firmware consists of three applications:
  NTAG_I2C_Explorer_Bootloader
  Jumps to the start memory of the user application. Enter into Flashing mode functionality. Enter into USB mode (Peek and Poke).
  NTAG_I2C_Explorer_Demo
  This project implements the logic supporting the Android / Windows demonstration applications
  NTAG_I2C_Explorer_Blink
  This application is provided to illustrate the NFC flashing functionality

## Slide 51: NTAG I²C plus Android Demo Application Screen: LEDDemo – 1.7.5 and upper
Select a LED colour which should light up on demoboard or switch off LED
Onboard temp. sensor can be enabled/disabled
LCD can be enabled/disabled as well as NDEF message appearance on LCD
Reads back:
  Temperature
  Energy Harvesting Voltage Vout
NXP logo colours changing dependent on button pressed on Demoboard

## Slide 52: PC Software – PC App
Together with the USB reader, the Windows app can be utilized to substitute a missing NFC mobile phone. The Windows app has identical functionalities as the Android app.
Will be available from NXP
public website

## Slide 53: PC Software – Peek & Poke
The Peek and Poke GUI is a Windows app that can be used to examine the detailed memory contents of the NTAG I2C EEPROM via I2C interface.

## Slide 54: Software sources (link active/online mid February) www.nxp.com/demobaord/OM5569
Title | Link
Source files | 
Android app (Eclipse project, works with Android studio) source | download
PC app (c# - Visual Studio) source | download
Peek and poke sources | download
Firmware for Explorer board includes: | download
NTAG I²C PLUS API | 
NTAG_I2C_Explorer_Bootloader | 
NTAG_I2C_Explorer_Demo | 
NTAG_I2C_Explorer_Blink | 

## Slide 55: NTAG I²C plus documents (link active/online mid February) http://www.nxp.com/products/NT3H2111_2211
Title | Link
Application notes | 
NTAG Antenna Design Guide | AN11276
NTAG21x Originality Signature Validation | AN11350
NTAG I²C Energy Harvesting | AN11578
How to use NTAG I²C (plus) for bidirectional communication | AN11579
NTAG I²C plus Memory Configuration Options | AN11786
User guides | 
NTAG I²C plus Explorer Kit and Android Demo | UM10966
NTAG I²C plus Explorer Kit and Peek & Poke | UM10967
*
*
*
*
* Available in DocStore already!
*

## Slide 56
www.nxp.com/nfc

## Slide 57
Thank You